## Slide 1: Conditional Processing
Eric Rees
Texas Tech University Spring 2021

## Slide 2: Uppercase <-> Lowercase
How do you think letters get converted upper case <-> lower case?
  Add / Subtract a certain value from the ASCII value?
How many letters in the English alphabet?
  26
ASCII value for A?
  65 (41h)
ASCII value for a?
  97 (61h)
97-65 = 32
Why 32 instead of 26?

## Slide 3: Select Boolean Instructions
Instruction | Description
AND | Boolean AND operation between a source operand and a destination operand.
OR | Boolean OR operation between a source operand and a destination operand.
XOR | Boolean exclusive-OR operation between a source operand and a destination operand.
NOT | Boolean NOT operation on a destination operand.
TEST | Implied Boolean AND operation between a source and destination operand, setting the CPU flags appropriately.

## Slide 4: CPU Status Flags
Boolean Instructions affect the following flags:
  Zero
  Carry
  Sign
  Overflow
  Parity

## Slide 5: AND Instruction
Performs a Boolean AND operation between each pair of matching bits in two operands.
Syntax:
AND destination, source
Allowed Combinations
AND reg,reg
AND reg,mem
AND reg,imm
AND mem,reg
AND mem,imm
  Immediate operands can be no larger than 32 bits.
  Operands can be 8, 16, 32, or 64 bits and must be same size.
The AND instruction lets you clear 1 or more bits in an operand without affecting other bits.

## Slide 6: AND Instruction - Flags
AND always clears the Overflow and Carry flags.
AND modifies the Sign, Zero, and Parity flags to be consistent with the value assigned to the destination operand.

## Slide 7: AND Instruction – Example
Problem
  Convert the character in AL to upper case.
Solution
  Use the AND instruction to clear bit 5 (0 based counting)
  mov al, ‘a’ ; AL = 01100001b (61h = ‘a’)
  and al, 11011111b ; AL = 01000001b (41h = ‘A’)
  and al, 11011111b ; AL = 01000001b – Unchanged!
01100001
AND 11011111
01000001

## Slide 8: OR Instruction
Performs a Boolean OR operation between each pair of matching bits in two operands.
Syntax:
OR destination, source
Allowed Combinations
OR reg,reg
OR reg,mem
OR reg,imm
OR mem,reg
OR mem,imm
  Operands can be 8, 16, 32, or 64 bits and must be same size.
The OR instruction lets you set 1 or more bits in an operand without affecting other bits.

## Slide 9: OR Instruction - Flags
OR always clears the Overflow and Carry flags.
OR modifies the Sign, Zero, and Parity flags to be consistent with the value assigned to the destination operand.

## Slide 10: OR Instruction – Example
Problem
  Convert the character in AL to lower case.
Solution
  Use the OR instruction to set bit 5 (0 based counting).
  mov al, ‘A’ ; AL = 01000001b (41h = ‘A’)
  or al, 00100000b ; AL = 01100001b (61h = ‘a’)
  or al, 00100000b ; AL = 01100001b - Unchanged
01000001
OR 00100000
01100001

## Slide 11: XOR Instruction
Performs a Boolean exclusive-OR operation between each pair of matching bits in two operands.
Syntax:
XOR destination, source
Allowed Combinations
XOR reg,reg
XOR reg,mem
XOR reg,imm
XOR mem,reg
XOR mem,imm
  Operands can be 8, 16, 32, or 64 bits and must be same size.

## Slide 12: XOR Instruction - Flags
XOR always clears the Overflow and Carry flags.
XOR modifies the Sign, Zero, and Parity flags to be consistent with the value assigned to the destination operand.

## Slide 13: XOR Instruction – Example
Example
  mov al, 10011010b ; AL = 10011010b
  xor al, 00001111b ; AL = 10010101b
  xor al, 00001111b ; AL = 10011010b
10011010
XOR 00001111
10010101

## Slide 14: NOT Instruction
Performs a Boolean NOT operation on all bits in an operand.
  Result is the one’s complement.
Syntax:
NOT destination
Allowed Combinations
XOR reg
XOR mem
NOT does not affect any flags.

## Slide 15: NOT Instruction – Example
Example
  mov al, 11110000b ; AL = 11110000b
  not al ; AL = 00001111b
  not al ; AL = 11110000b

## Slide 16: TEST Instruction
Performs an implied Boolean AND operation between each pair of matching bits in two operands.
Syntax:
TEST destination, source
Allowed Combinations
TEST reg,reg
TEST reg,mem
TEST reg,imm
TEST mem,reg
TEST mem,imm
  Immediate operands can be no larger than 32 bits.
  Operands can be 8, 16, 32, or 64 bits and must be same size.
Only difference between TEST and AND is that TEST does not modify the destination operand.

## Slide 17: TEST Instruction - Flags
TEST always clears the Overflow and Carry flags.
TEST modifies the Sign, Zero, and Parity flags to be consistent with the value assigned to the destination operand.

## Slide 18: TEST Instruction – Example
Problem
  Test is bit 0 or bit 3 are set in register AL.
Solution
  Use the TEST operand and check the zero flag.
  mov al, 11100100b ; AL = 11100100b
  test al, 00001001b ; result = 00000000 | ZF = 1
  mov al, 11111000b ; AL = 11111000b
  test al, 00001001b ; result = 00001000 | ZF = 0

## Slide 19: CMP Instruction
Compares integers to determine less than, greater than or equal to.
Performs nondestructive subtraction of source from destination. Destination is left unchanged.
Syntax:
CMP destination, source
Allowed Combinations
  Same as AND

## Slide 20: CMP Instruction - Flags
CMP changes the Overflow, Sign, Zero, Carry, Auxiliary Carry, and Parity flags as if the source was subtracted from the destination – though true subtraction doesn’t take place.
When comparing two unsigned operands, the Zero and Carry flags indicate the following relations between operands:
When comparing two signed operands, the Sign, Zero, and Overflow flags indicate the following relations between operands:
CMP Results | ZF | CF
Destination < Source | 0 | 1
Destination > Source | 0 | 0
Destination = Source | 1 | 0
CMP Results | Flags
Destination < Source | SF ≠ OF
Destination > Source | SF = OF
Destination = Source | ZF = 1

## Slide 21: CMP Instruction - Example
Example using unsigned operands:
  mov al, 4
; Destination < Source
cmp al, 5 ; CF = 1, SF = 1, ZF = 0, OF = 0
; Destination > Source
cmp al, 3 ; CF = 0, SF = 0, ZF = 0, OF = 0
; Destination == Source
cmp al, 4 ; CF = 0, SF = 0, ZF = 1, OF = 0

## Slide 22: CMP Instruction - Example
Example using signed operands:
  mov al, -1
; Destination < Source
cmp al, 5 ; CF = 0, SF = 1, ZF = 0, OF = 0 SF != OF
; Destination > Source
cmp al, -5 ; CF = 1, SF = 0, ZF = 0, OF = 0 SF == OF
; Destination == Source
cmp al, -1 ; CF = 0, SF = 0, ZF = 1, OF = 0 ZF = 1

## Slide 23: Set/Clear Individual CPU Flags
Using Boolean operations or other instructions, we can easily set or clear the following flags:
  Zero
  Sign
  Carry
  Overflow

## Slide 24: Set/Clear the Overflow Flag
To set the Zero flag, TEST or AND an operand with 0.
To clear the Zero flag, OR an operand with 1.
Example:
test al,0 ; set Zero flag
and al,0 ; set Zero flag
or al,1 ; clear Zero flag

## Slide 25: Set/Clear the Sign Flag
To set the Sign flag, OR the highest bit of an operand with 1.
To clear the Sign flag, AND the highest bit of an operand with 0.
Example:
or al,80h ; set Sign flag
and al,7Fh ; clear Sign flag

## Slide 26: Set/Clear the Carry Flag
To set the Carry flag, use the STC (SeT Carry) instruction.
To clear the Carry flag, use the CLC (CLear Carry) instruction.
Example:
stc ; Set the Carry Flag
clc ; Clear the Carry Flag

## Slide 27: Set/Clear the Overflow Flag
To set the Overflow flag, add two positive values that produce a negative sum.
To clear the Overflow flag, or an operand with 0.
Example:
mov al, 7Fh ; AL = +127
inc al ; AL = 80h (+128 Unsigned, -128 Signed), OF=1
or al,0 ; Clear the Overflow Flag

## Slide 28: Required Reading
Read the “Conditional Jumps” (6.2) section of your book and pay careful attention to the multitude of new “Jcond” instructions. You need to also type in and test the examples found in section 6.2.4.
  We do not have time in this course to sit and discuss every single instruction and provide examples.
  You may be tested on ANY of the “Jcond” instructions mentioned in this section

## Slide 29: Conditional Structures and Jcond
x86 Assembly does not have block-oriented conditional instructions such as IF, ELSE, ELIF, or ENDIF.
However, you can implement conditional structures using a combination of comparisons and jumps.
  First, an operation such as CMP, AND, or SUB modifies the CPU flags.
  Second, a conditional jump instruction tests the flags and causes a branch to a new address.
Conditional Jump (Jcond Instruction)
  Branches to a destination label when a status flag condition is true.
  Otherwise, if the flag condition is false, the next instruction following the conditional jump is executed.

## Slide 30: Jcond
Jcond the name given to the numerous J<condition> Instructions that exist in x86 assembly. Jcond itself is not an instruction.
  cond refers to a flag condition identifying the state of one or more flags.
General syntax for all Jcond instructions:
Jcond destination
Types of Conditional Jumps:
  Jumps based on specific flag values.
  Jumps based on equality between operands or the value of RCX, ECX, or CX
  Jumps based on comparisons of unsigned operands
  Jumps based on comparisons of signed operands

## Slide 31: Jumps Based on Specific Values
Instruction | Description | Flags / Registers
JZ | Jump if zero | ZF = 1
JNZ | Jump if not zero | ZF = 0
JC | Jump if carry | CF=1
JNC | Jump if not carry | CF=0
JO | Jump if overflow | OF=1
JNO | Jump if not overflow | OF=0
JS | Jump if signed | SF=1
JNS | Jump if not signed | SF=0
JP | Jump if parity (even) | PF=1
JNP | Jump if not parity (odd) | PF=0

## Slide 32: Jumps Based on Equality
Instruction | Description
JE | Jump if equal (destination = source)
JNE | Jump if not equal (destination ≠ source)
JCXZ | Jump if CX=0
JECXZ | Jump if ECX=0
JRCXZ | Jump if RCX=0 (64−bit mode)

## Slide 33: Jumps Based on Unsigned Comparisons
Instruction | Description
JA | Jump if above (if destination > source)
JNBE | Jump if not below or equal (same as JA)
JAE | Jump if above or equal (if destination ≥ source)
JNB | Jump if not below (same as JAE)
JB | Jump if below (if destination < source)
JNAE | Jump if not above or equal (same as JB)
JBE | Jump if below or equal (if destination ≤ source)
JNA | Jump if not above (same as JBE)

## Slide 34: Jumps Based on Signed Comparisons
Instruction | Description
JG | Jump if greater (if destination > source)
JNLE | Jump if not less than or equal (same as JG)
JGE | Jump if greater than or equal (if destination ≥ source)
JNL | Jump if not less (same as JGE)
JL | Jump if less (if destination < source)
JNGE | Jump if not greater than or equal (same as JL)
JLE | Jump if less than or equal (if destination ≤ source)
JNG | Jump if not greater (same as JLE)

## Slide 35: Jcond Instructions - Example
mov edx, 0A523h
cmp edx, 0A523h
jne J1 ; Jump not taken
je J2 ; Jump is taken

## Slide 36: Jcond Instructions - Example
mov bx, 1234h
sub bx, 1234h
jne J3 ; Jump not taken
je J4 ; Jump is taken
; Remember, Equality is when ZF = 1 and CF = 0

## Slide 37: Jcond Instructions - Example
mov cx, 0FFFFh
jcxz J5 ; Jump not taken
inc cx
jcxz J6 ; Jump is taken

## Slide 38: Jcond Instructions - Example
mov edx,-1024
cmp edx,0
jnl J1 ; jump not taken (-1 >= 0 is false)
jnle J2 ; jump not taken (-1 > 0 is false)
jl J3 ; jump is taken (-1 < 0 is true)

## Slide 39: Jcond Instructions - Example
mov bx,+32
cmp bx,-35
jng L5 ; jump not taken (+32 <= -35 is false)
jnge L5 ; jump not taken (+32 < -35 is false)
jge L1 ; jump is taken (+32 >= -35 is true)
; This example has a possible logical fallacy – what is it?
; - If the numbers are equal it will go to L5, not L1.
; - This might be what we expected, it might not.

## Slide 40: Jcond Instructions - Example
mov ecx,0
cmp ecx,0
jg L5 ; jump not taken (0 > 0 is false)
jnl L1 ; jump is taken (0 >= 0 is true)

## Slide 41: LOOPZ and LOOPE
Loop if zero/equal. Identical instructions.
Works the same as LOOP with 1 additional condition – the Zero flag must be set in order for transfer of control to transfer to the destination.
Syntax:
  LOOPZ destination
Logic:
  ECX = ECX – 1
  If ECX > 0 and ZF = 1, jump to destination.
  Else control passes to next instruction.

## Slide 42: LOOPNZ and LOOPNE
Loop if not zero/equal. Identical instructions.
Works the same as LOOP with 1 additional condition – the Zero flag must be clear in order for transfer of control to transfer to the destination.
Syntax:
  LOOPNZ destination
Logic:
  ECX = ECX – 1
  If ECX > 0 and ZF = 0, jump to destination.
  Else control passes to next instruction.

## Slide 43: Conditional Structures
A combination of assembly language statements that use Boolean conditions to determine whether a certain block of statements will execute.
Common Structures:
  IF / ELSE
  IF / ELSE-IF / ELSE
  While
These high-level programming constructs don’t exist in Assembly and must instead be constructed using conditional/unconditional jumps.

## Slide 44: Semantic Actions for if-else Statements Modified from my CS1411 (Python) course notes
Upon encountering the if keyword, the interpreter will begin evaluating the condition.
The interpreter will continue to evaluate the condition until it encounters an error or completes enough of the condition to ensure a valid answer – even if this means not evaluating the entire expression!
If the condition evaluates to true, the body of python code following the if statement will begin execution starting from the first line.
  Execution will continue until the if statement encounters the end of the statement’s body.
  Upon encountering the end of the if statement’s body, the program will continue execution starting with the first line after the end of the body.
  If the next line after the end of the body contains an ‘else’ statement, the program will skip over the else statement (and the else statement’s body) and begin execution at the first line following the else statement’s body.
If the condition evaluates to false, the body of python code following the if statement will be skipped and execution will begin starting from the first line after the end of the if statement’s body.
  If the first line encountered is an ‘else’ statement, the interpreter will execute the body of code under the else statement starting with the first line.
  Execution will continue until the else statement encounters the end of the statement’s body.
  Upon encountering the end of the else statement’s body, the program will continue execution starting with the first line after the end of the body.

## Slide 45: Compound Expressions
An expression involving two or more subexpressions, usually Boolean ones, joined together using AND, OR, and NOT.
These rely on logical AND, logical OR, and logical NOT.
Sadly, these logical operators do not exist in Assembly language…
So how do we build compound expressions?

## Slide 46: Short-Circuit Evaluation
Before discussing compound expressions, let’s first discuss Short-Circuit Evaluation.
What is it?
  Let’s revisit a line from the semantic actions for If-Else: “The interpreter will continue to evaluate the condition until it encounters an error or completes enough of the condition to ensure a valid answer – even if this means not evaluating the entire expression!”
Short Circuit Evaluation is found in all modern high-level languages.
  It prevents the CPU from wasting time comparing items when the result would not change the final answer.

## Slide 47: Short-Circuit Evaluation
Short-Circuit Evaluation (AND)
  Evaluation of the compound AND operator in which the right-hand expression is not evaluated if the left-hand expression is false.
Short-Circuit Evaluation (OR)
  Evaluation of the compound OR operator in which the right-hand expression is not evaluated if the left-hand expression is true.

## Slide 48: Logical AND Operator
C++ Code
if (al > bl) && (bl > cl) {
X = 1;
}
Assembly
cmp al, bl ; Compare al/bl
ja L1 ; al > bl?
jmp next ; al > bl = False
L1: ; al > bl = True
cmp bl, cl ; Compare bl/cl
ja L2 ; bl > cl?
jmp next ; bl > cl = False
L2: ; bl > cl = True
mov X,1
next:

## Slide 49: Logical AND Operator
Assembly
cmp al, bl ; Compare al/bl
ja L1 ; al > bl?
jmp next ; al > bl = False
L1: ; al > bl = True
cmp bl, cl ; Compare bl/cl
ja L2 ; bl > cl?
jmp next ; bl > cl = False
L2: ; bl > cl = True
mov X,1
next:
Assembly (Optimized)
cmp al, bl ; Compare al/bl
jbe next ; al <= bl?
cmp bl, cl ; Compare bl/cl
jbe next ; bl <= cl?
mov X, 1
next:

## Slide 50: Logical OR Operator
C++ Code
if (al > bl) || (bl > cl) {
X = 1;
}
Assembly (Optimized)
cmp al, bl ; Compare al/bl
ja L1 ; al > bl?
cmp bl, cl ; Compare bl/cl
jbe next ; False, skip
L1: ; True
mov X,1 ; set X = 1
next:

## Slide 51: WHILE Loops
C++ Code
while ( val1 < val2 )
{
val1++;
val2--;
}
Assembly
mov eax,val1 ; eax = val1
beginwhile:
cmp eax,val2 ; Compare val1/val2
jnl endwhile ; not (val1 < val2)?
inc eax ; val1++
dec val2 ; val2--
jmp beginwhile ; Return to top
endwhile:
mov val1,eax ; val1 = eax

## Slide 52: Required Reading
Read the “Conditional Structures” (6.4) section of your book and run through some of the examples.
  Make sure to read Section 6.4.3 and work through the Example “IF statement Nested in a Loop”.
  Try to build the code for this example using the provided flowchart BEFORE looking at the code.
  Expect to see a similarly built code comprehension question!

## Slide 53: Example: IF/ELSE
Construct the following IF/ELSE conditional structure in Assembly.
C++ Code:
if ( op1 == op2 ) {
X = 1;
Y = 2;
}
else {
X = 2;
Y = 1;
}

## Slide 54: Example: IF/ELSE w/ Procedures
Write a test program that generates 10 random integers between 50 and 100, inclusive.
Each time an integer is generated, pass it to a procedure that determines the letter grade.
Use the book's library to display each integer and its corresponding letter grade.